The black text is taken directly from an example config.json file (except for the equations) and the blue text has been added as explanation

{
"AUTO_EXPOSURE" : "Off", this should default to off but should still be adjustable Off,On
"EXPOSURE" : 8999, if Auto exposure is On then this one shouldn’t be set any floating point < 999998.00
"AUTO_GAIN" : "Off", this should default to off but should still be adjustable Off,On
"GAIN" : 10, if Auto exposure is On then this one shouldn’t be set floating point 0.00-40.00

"WIDTH" : 600, integer > 8 and <
as any multiple of 8
"HEIGHT" : 490, integer > 8 and <
as any even number

The two offset values get set to 0 to start with to allow the width and height to be set without restrictions then get set as the last step of initialisation.

"OFFSET_X" : 8, default value for this is 8 but can be any multiple of 8
.

"OFFSET_Y" : 20, the optimal value is determined by
but can also be any even integer

"BIT_DEPTH" : "Mono8", this can be one of 3 strings “Mono8”, “Mono12p”, “Mono16”
"ADC_BIT_DEPTH" : "Bit8", this can be one of 3 strings “Bit8”, “Bit10”, “Bit12”
"BINS" : 4, integer 1, 2 or 4
"ISP" : "True", if BINS >2 this should have the value “True” if BINS < 2 this should have the value “False”
"BIN_METHOD" : "Average", default setting Average, can be either “Average” or “Sum”
"DECIMATION" : 1, this is actually unnecessary so just ignore it
"ACQUISITION_MODE" : "trigger", default “trigger”can be one of 3 strings “trigger”, “time”, “continuous”
"ACQUISITON_TIME": 10, any integer (its in seconds)
}